## Slide 1: Assembly Language Programming in 8086 Microprocessor
Assembly Language

## Slide 2: Program Conversion in CPU
High Level Language
Assembly Code
Object File (Contains Source Code )
Machine Code
Hardware
Assembler
Library File
Linker
Compiler

## Slide 3: Addressing Modes
2 + 2
2 and 2 are operands
+ is an opcode (operational code).
In Assembly Language, Opcode would be come before registers
Registers Addressing – Both operands are registers
Immediate Addressing – One operand is constant term
Memory Addressing – Access static data directly

## Slide 4: Data Transfer Instruction
MOV Instruction
  The MOV instruction is the most important command in the 8086 because it moves data from one location to another
  It also has the widest variety of parameters; so if the assembler programmer can use MOV effectively, the rest of the commands are easier to understand.
  Example: MOV DL , 2
          MOV Ah , 2

## Slide 5: Service Routine
1 = input a character with echo
2 = Output or print a character
8 = Input a character without echo
9 = Output or print collection of characters (String)
4ch = Exit

## Slide 6: Interrupt
Stop the current program and allow microprocessor to access hardware to take input or give output.
INT 21H = Interrupt for text handling
INT 20H for video or graphic handling
Example :
MOV Ah, 2 INT 21H | MOV Ah, 1 INT 21H | MOV Ah, 8 INT 21H

## Slide 7: ASCII Code
American Standard Code for Information Interchange
Character Encoding Scheme
By American Standards Association
Published in 1963
A = 65 to Z = 90
a = 97 to z = 122
0 = 48 to 9 = 57

## Slide 8: Program Structure
.Model memory-model
  Reserve the space of the Assembly code in RAM.
  Enables use of simplified segments
  Determine the size of Code Segment and Data Segment
Memory Models | Code Size | Data Size
Tiny | Code <=32KB | Data <=32KB
Small | Code <=64KB | Data <=64KB
Medium | Code = Any size | Data <=64KB
Compact | Code <=64KB | Data = Any size
Large | Code = Any size | Data = Any size
Huge | Code = Any size | Data = Any size

## Slide 9: Program Structure
.Stack size
  Reserve 256 bytes of stack space
  Specifies the storage for stack where the size is optional.
  Default is 1024 bytes
  Tells the assembler to define a runtime stack for the program
.Data
  Define an area in memory for the program data
  Program’s variables should be defined under this directive
  Assembler will allocate and initialize the storage of variables in the data segment in the memory

## Slide 10: Program Structure
.Code
  Define the code section of a program containing executable instructions
  Assembler will place the instructions in the code segment in the memory
Main procedure-name
  Collection of instructions to which we can direct the flow of our program.
  Once the flow of the program has been transferred and the procedure is done, One can return to the next line
dosseg
  It is a DOS segment which manage all the arrangement of segments in a program, if in case we have forgot to write in programs in a sequence

## Slide 11: Sample Program
.model small ;Model Directive
.stack 100h ;Stack Segment Directive
.data ;Data Segment Directive
.code ;Code Segment Directive
Main proc ;Procedure call
Main endp ;Procedure end
End Main ;Program exit

## Slide 12: Syntax Rules
Space after Opcode
One operand must be general purpose register
Operands must be of same size
Comma between operands
  Mov ‘B’, ‘A’ X
  Mov 2, 3 X
  Mov dl, AX X
  Mov dl, ‘A’ √
  Mov dx, AX √
  Mov dh, al √
  Mov dh, 3 √

## Slide 13: Program to print a single character on screen?
dosseg
.model small
.stack 100h
.data
.code
Main proc
Mov dl, ‘A’
Mov ah, 2
Int 21h
Mov ah, 4ch
Int 21h
Main endp
End Main

## Slide 14: Program to print a single character on screen?
dosseg
.model small
.stack 100h
.data
.code
Main proc
Mov ah, 1
Int 21h
Mov dl, al
Mov ah, 2
Int 21h
Mov ah, 4ch
Int 21h
Main endp
End Main

## Slide 15: Program to print collection of characters on screen?
dosseg
.model small
.stack 100h
.data
msg db ‘Hello World$’
.code
Main proc
Mov ax, @data
Mov ds, ax
LEA dx, msg
Mov ah, 9
Int 21h
Mov ah, 4ch
Int 21h
Main endp
End Main

## Slide 16
Program to print your name with character on screen?
dosseg
.model small
.stack 100h
.data
.code
Main proc
Mov dl, ‘S’
Mov ah, 2
Int 21h
Mov dl, ‘A’
Mov ah, 2
Int 21h
Mov dl, ‘L’
Mov ah, 2
Int 21h
Mov dl, ‘W’
Mov ah, 2
Int 21h
Mov dl, ‘A’
Mov ah, 2
Int 21h
Mov ah, 4ch
Int 21h
Main endp
End Main

## Slide 17
Program to add two numbers?
dosseg
.model small
.stack 100h
.data
.code
Main proc
Mov bl, 1
Mov cl, 2
Add bl, cl
Add bl, 48
Mov dl, bl
Mov ah, 2
Int 21h
Mov ah, 4ch
Int 21h
Main endp
End Main

## Slide 18
Program to subtract two numbers?
dosseg
.model small
.stack 100h
.data
.code
Main proc
Mov bl, 3
Mov cl, 1
Sub bl, cl
Add bl, 48
Mov dl, bl
Mov ah, 2
Int 21h
Mov ah, 4ch
Int 21h
Main endp
End Main

## Slide 19
Program to input two numbers and add them?
dosseg
.model small
.stack 100h
.data
.code
Main proc
Mov ah, 1
Int 21h
Mov bl, al
Mov ah, 1
Int 21h
Add bl, al
Sub bl, 48
Mov dl, bl
Mov ah, 2
Int 21h
Mov ah, 4ch
Int 21h
Main endp
End Main

## Slide 20
Program to input two numbers and subtract them?
dosseg
.model small
.stack 100h
.data
.code
Main proc
Mov ah, 1
Int 21h
Mov bl, al
Mov ah, 1
Int 21h
Sub bl, al
Add bl, 48
Mov dl, bl
Mov ah, 2
Int 21h
Mov ah, 4ch
Int 21h
Main endp
End Main

## Slide 21
Program to convert capital letter into small letter?
dosseg
.model small
.stack 100h
.data
.code
Main proc
Mov ah, 1
Int 21h
Mov dl al
Add dl, 32
Mov ah, 2
Int 21h
Mov ah, 4ch
Int 21h
Main endp
End Main

## Slide 22: Variables in programs
Variables are defined in .data directive in Assembly language of program structure.
The method to initialized variable in program would be
  Write Variable-Name first.
  Then, write Data-Size.
  Then, write Value in single quotation‘ ’.
Syntax: Variable-Name Data-Size ‘Value’

## Slide 23: Variable-Name in .data directive
Variable-Name is the identifier for each storage space.
Don’t use reserved keyword as Variable-Name
  AL, BL, CL, DL, …. X
  SUB, ADD, MUL, DIV, …. X
  MOV, LEA, PUSH, POP, …. X
Always use keyword like Var1, Var2, …. msg1, msg2, ….

## Slide 24: Data-Size in .data directive
Data-Size, also called Initialize directive which is used for reserving storage space for variables.
It can be used to reserve as well as initialize one or more bytes.
Directive | Purpose | Storage Space
db | Define Byte | 1 byte or 8 bits
dw | Define Word | 2 bytes or 16 bits
dd | Define Double Word | 4 bytes or 32 bits
dq | Define Quad Word | 8 bytes or 64 bits
dt | Define Ten Bytes | 10 bytes or 80 bits

## Slide 25: Data-Size in .data directive
Each byte of character is stored as its ASCII value in hexadecimal.
? sign shows that there is nothing assigned in .data directive and you have to initialized in .code directive
$ sign, also called terminator must be used in end of the string.
Variable-Name | Data-Size | Value
Var1 | db | 49
Var1 | db | ‘1’
Var1 | db | ‘A’
Var1 | db | ?
Var1 | db | ‘1234$’

## Slide 26: Program to print multiple variables on screen?
dosseg
.model small
.stack 100h
.data
Var1 db ‘1’
Var2 db ?
Var3 db ‘1234$’
.code
Main proc
Mov ax, @data
Mov ds, ax
Mov dl, Var1
Mov ah, 2
Int 21h
Mov Var2, bl
LEA dx, Var3 OR Mov dx, Offset Var3
Mov ah, 9
Int 21h
Mov ah, 4ch
Int 21h
Main endp
End Main

## Slide 27: Program to print two different strings on two different lines
dosseg
.model small
.stack 100h
.data
msg1 db ‘HELLO$’
msg2 db ‘WORLD$’
.code
Main proc
Mov ax, @data
Mov ds, ax
LEA dx, msg1
Mov ah, 9
Int 21h
Mov dx, 10 ;NEW LINE FEED
Mov ah, 2
Int 21h
Mov dx, 13 ;CARRIAGE RETURN
Mov ah, 2
Int 21h
LEA dx, msg2
Mov ah, 9
Int 21h
Mov dx, 10
Mov ah, 2
Int 21h
Mov dx, 13
Mov ah, 2
Int 21h
Mov ah, 4ch
Int 21h
Main endp
End Main

## Slide 28: Loops in programs
Series of instructions that is repeated until a terminating condition is reached is called Loop.
Counter Register CX is used as a loop counter.
Before the series of instruction, give the name at the beginning which is called Label.
Example:
      LabelName: Identification of the below series of instructions
      Mov dx, ‘a’
      Mov ah, 2
      Int 21h
      Loop LabelName Loop is calling the series of instruction here

## Slide 29: Label rules in programs
Label can be placed at the beginning of a statement, because the label is assigned the current value of line.
Label name must not be a reserved keyword. E.g. Mov, Add, DB, DW etc.
Colon : must be used with Label while initializing, but not while calling.

## Slide 30: Program to print 0 to 9 numbers
dosseg
.model small
.stack 100h
.data
.code
Main proc
Mov cx, 10
Mov dx, 48
Label1:
Mov ah, 2
Int 21h
Inc dx OR Add dx, 1
Loop Label1
Mov ah, 4ch
Int 21h
Main endp
End Main